## Slide 1: Slide Deck 12
ECE 4203 VLSI Design

## Slide 2: Outline
Sequencing
Sequencing Element Design
Max and Min-Delay
Clock Skew
Time Borrowing
Two-Phase Clocking

## Slide 3: Sequencing
Combinational logic
  output depends on current inputs
Sequential logic
  output depends on current and previous inputs
  Requires separating previous, current, future
  Called state or tokens
  Ex: FSM, pipeline

## Slide 4: Sequencing Cont.
If tokens moved through pipeline at constant speed, no sequencing elements would be necessary
Ex: fiber-optic cable
  Light pulses (tokens) are sent down cable
  Next pulse sent before first reaches end of cable
  No need for hardware to separate pulses
  But dispersion sets min time between pulses
This is called wave pipelining in circuits
In most circuits, dispersion is high
  Delay fast tokens so they don’t catch slow ones.

## Slide 5: Sequencing Overhead
Use flip-flops to delay fast tokens so they move through exactly one stage each cycle.
Inevitably adds some delay to the slow tokens
Makes circuit slower than just the logic delay
  Called sequencing overhead
Some people call this clocking overhead
  But it applies to asynchronous circuits too
  Inevitable side effect of maintaining sequence

## Slide 6: Sequencing Elements
Latch: Level sensitive
  a.k.a. transparent latch, D latch
Flip-flop: edge triggered
  A.k.a. master-slave flip-flop, D flip-flop, D register
Timing Diagrams
  Transparent
  Opaque
  Edge-trigger

## Slide 7: Latch Design
Pass Transistor Latch
Pros
  + Tiny
  + Low clock load
Cons
  Vt drop
  nonrestoring
  backdriving
  output noise sensitivity
  dynamic
  diffusion input
Used in 1970’s

## Slide 8: Latch Design
Transmission gate
  + No Vt drop
  - Requires inverted clock

## Slide 9: Latch Design
Inverting buffer
  + Restoring
  + No backdriving
  + Fixes either
    Output noise sensitivity
    Or diffusion input
  Inverted output

## Slide 10: Latch Design
Tristate feedback
  + Static
  Backdriving risk
Static latches are now essential
because of leakage

## Slide 11: Latch Design
Buffered input
  + Fixes diffusion input
  + Noninverting

## Slide 12: Latch Design
Buffered output
  + No backdriving
Widely used in standard cells
  + Very robust (most important)
  Rather large
  Rather slow (1.5 – 2 FO4 delays)
  High clock loading

## Slide 13: Latch Design
Datapath latch
  + smaller
  + faster
  - unbuffered input

## Slide 14: Flip-Flop Design
Flip-flop is built as pair of back-to-back latches

## Slide 15: Enable
Enable: ignore clock when en = 0
  Mux: increase latch D-Q delay
  Clock Gating: increase en setup time, skew

## Slide 16: Reset
Force output low when reset asserted
Synchronous vs. asynchronous

## Slide 17: Set / Reset
Set forces output high when enabled
Flip-flop with asynchronous set and reset

## Slide 18: Sequencing Methods
Flip-flops
2-Phase Latches
Pulsed Latches

## Slide 19: Timing Diagrams
tpd | Logic Prop. Delay
tcd | Logic Cont. Delay
tpcq | Latch/Flop Clk->Q Prop. Delay
tccq | Latch/Flop Clk->Q Cont. Delay
tpdq | Latch D->Q Prop. Delay
tcdq | Latch D->Q Cont. Delay
tsetup | Latch/Flop Setup Time
thold | Latch/Flop Hold Time
Contamination and Propagation Delays

## Slide 20: Max-Delay: Flip-Flops

## Slide 21: Max Delay: 2-Phase Latches

## Slide 22: Max Delay: Pulsed Latches

## Slide 23: Min-Delay: Flip-Flops

## Slide 24: Min-Delay: 2-Phase Latches
Hold time reduced by nonoverlap
Paradox: hold applies twice each cycle, vs. only once for flops.
But a flop is made of two latches!

## Slide 25: Min-Delay: Pulsed Latches
Hold time increased by pulse width

## Slide 26: Time Borrowing
In a flop-based system:
  Data launches on one rising edge
  Must setup before next rising edge
  If it arrives late, system fails
  If it arrives early, time is wasted
  Flops have hard edges
In a latch-based system
  Data can pass through latch while transparent
  Long cycle of logic can borrow time into next
  As long as each loop completes in one cycle

## Slide 27: Time Borrowing Example

## Slide 28: How Much Borrowing?
2-Phase Latches
Pulsed Latches

## Slide 29: Clock Skew
We have assumed zero clock skew
Clocks really have uncertainty in arrival time
  Decreases maximum propagation delay
  Increases minimum contamination delay
  Decreases time borrowing

## Slide 30: Skew: Flip-Flops

## Slide 31: Skew: Latches
2-Phase Latches
Pulsed Latches

## Slide 32: Two-Phase Clocking
If setup times are violated, reduce clock speed
If hold times are violated, chip fails at any speed
In this class, working chips are most important
  No tools to analyze clock skew
An easy way to guarantee hold times is to use 2-phase latches with big nonoverlap times
Call these clocks f1, f2 (ph1, ph2)

## Slide 33: Safe Flip-Flop
Past years used flip-flop with nonoverlapping clocks
  Slow – nonoverlap adds to setup time
  But no hold times
In industry, use a better timing analyzer
  Add buffers to slow signals if hold time is at risk

## Slide 34: Adaptive Sequencing
Designers include timing margin
  Voltage
  Temperature
  Process variation
  Data dependency
  Tool inaccuracies
Alternative: run faster and check for near failures
  Idea introduced as “Razor”
    Increase frequency until at the verge of error
    Can reduce cycle time by ~30%

## Slide 35: Summary
Flip-Flops:
  Very easy to use, supported by all tools
2-Phase Transparent Latches:
  Lots of skew tolerance and time borrowing
Pulsed Latches:
  Fast, some skew tol & borrow, hold time risk