## Slide 1: Slide Deck 15
ECE 4203 VLSI Design

## Slide 2: Outline
Clock System Architecture
Phase-Locked Loops
Delay-Locked Loops

## Slide 3: Clock Generation
Low frequency:
  Buffer input clock and drive to all registers
High frequency
  Buffer delay introduces large skew relative to input clocks
    Makes it difficult to sample input data
  Distributing a very fast clock on a PCB is hard

## Slide 4: Zero-Delay Buffer
If the periodic clock is delayed by Tc, it is indistinguishable from the original clock
Build feedback system to guarantee this delay
Phase-Locked
Loop (PLL)
Delay-Locked
Loop (DLL)

## Slide 5: Frequency Multiplication
PLLs can multiply the clock frequency
  Distribute a lower frequency on the board
  Multiply it up on-chip
  Possible to adjust the frequency on the fly

## Slide 6: Phase and Frequency
Analyze PLLs and DLLs in term of phase F(t) rather than voltage v(t)
Input and output clocks may
deviate from locked phase
  Small signal analysis

## Slide 7: Linear System Model
Treat PLL/DLL as a linear system
  Compute deviation DF from locked position
  Assume small deviations from locked
  Treat system as linear for these small changes
Analysis is not valid far from lock
  e.g. during acquisition at startup
Continuous time assumption
  PLL/DLL is really a discrete time system
    Updates once per cycle
  If the bandwidth << 1/10 clock freq, treat as continuous
Use Laplace transforms and standard analysis of linear continuous-time feedback control systems

## Slide 8: Phase-Locked Loop (PLL)
System
Linear Model

## Slide 9: Voltage-Controlled Oscillator
VCO
-
+

## Slide 10: Alternative Delay Elements

## Slide 11: Frequency Divider
Divide clock by N
  Use mod-N counter

## Slide 12: Phase Detector
Difference of input and
feedback clock phase
Often built from phase-frequency detector (PFD)

## Slide 13: Phase Detector
Convert up and down pulses into current proportional to phase error using a charge pump

## Slide 14: Loop Filter
Convert charge pump
current into Vctrl
Use proportional-integral control (PI) to generate a control signal dependent on the error and its integral
  Drives error to 0
(negligible)

## Slide 15: PLL Loop Dynamics
Closed loop transfer function of PLL
This is a second order system
wn indicates loop bandwidth
z indicates damping; choose 0.7 – 1 to avoid ringing

## Slide 16: Delay Locked Loop
Delays input clock rather than creating a new clock with an oscillator
Cannot perform frequency multiplication
More stable and easier to design
  1st order rather than 2nd
State variable is now time (T)
  Locks when loop delay is exactly Tc
  Deviations of DT from locked value

## Slide 17: Delay-Locked Loop (DLL)
System
Linear Model

## Slide 18: Delay Line
Delay input clock
Typically use voltage-controlled delay line

## Slide 19: Phase Detector
Detect phase error
Typically use PFD and charge pump, as in PLL

## Slide 20: Loop Filter
Convert error current
into control voltage
Integral control is sufficient
Typically use a capacitor as the loop filter

## Slide 21: DLL Loop Dynamics
Closed loop transfer function of DLL
This is a first order system
t indicates time constant (inverse of bandwidth)
  Choose at least 10Tc for continuous time approx.