## Slide 1: Slide Deck 16
ECE 4203 VLSI Design

## Slide 2: Midterm 2 Overview
Covers topics after Midterm #1
Four (4) Questions (adding up to 100 points)
  Sequential circuit
  Power consumption
  Interconnect
  Logical Path Effort
No Questions on
  PLL, DLL’s
  I/O
  SPICE simulation
  Thermal management, packaging
Extra Credit Question
  Debugging latch error as your first project at NVIDIA

## Slide 3: Multistage Logic Networks
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort

## Slide 4: Branching Effort
Introduce branching effort
  Accounts for branching between stages in path
Now we compute the path effort
  F = GBH
Note:

## Slide 5: Multistage Delays
Path Effort Delay
Path Parasitic Delay
Path Delay

## Slide 6: Designing Fast Circuits
Delay is smallest when each stage bears same effort
Thus minimum delay of N stage path is
This is a key result of logical effort
  Find fastest possible delay
  Doesn’t require calculating gate sizes

## Slide 7: Gate Sizes
How wide should the gates be for least delay?
Working backward, apply capacitance transformation to find input capacitance of each gate given load it drives.
Check work by verifying input cap spec is met.

## Slide 8: Example: 3-stage path
Select gate sizes x and y for least delay from A to B

## Slide 9: Example: 3-stage path
Logical Effort G = (4/3)*(5/3)*(5/3) = 100/27
Electrical Effort H = 45/8
Branching Effort B = 3 * 2 = 6
Path Effort F = GBH = 125
Best Stage Effort
Parasitic Delay P = 2 + 3 + 2 = 7
Delay D = 3*5 + 7 = 22 = 4.4 FO4

## Slide 10: Example: 3-stage path
Work backward for sizes
y = 45 * (5/3) / 5 = 15
x = (15*2) * (5/3) / 5 = 10

## Slide 11: Timing Diagrams
tpd | Logic Prop. Delay
tcd | Logic Cont. Delay
tpcq | Latch/Flop Clk->Q Prop. Delay
tccq | Latch/Flop Clk->Q Cont. Delay
tpdq | Latch D->Q Prop. Delay
tcdq | Latch D->Q Cont. Delay
tsetup | Latch/Flop Setup Time
thold | Latch/Flop Hold Time
Contamination and Propagation Delays

## Slide 12: Max-Delay: Flip-Flops

## Slide 13: Min-Delay: Flip-Flops

## Slide 14: Charging a Capacitor
When the gate output rises
  Energy stored in capacitor is
  But energy drawn from the supply is
  Half the energy from VDD is dissipated in the pMOS transistor as heat, other half stored in capacitor
When the gate output falls
  Energy in capacitor is dumped to GND
  Dissipated as heat in the nMOS transistor

## Slide 15: Activity Factor
Suppose the system clock frequency = f
Let fsw = af, where a = activity factor
  If the signal is a clock, a = 1
  If the signal switches once per cycle, a = ½
Dynamic power:

## Slide 16: Dynamic Power Example
1 billion transistor chip
  50M logic transistors
    Average width: 12 l
    Activity factor = 0.1
  950M memory transistors
    Average width: 4 l
    Activity factor = 0.02
  1.0 V 65 nm process
  C = 1 fF/mm (gate) + 0.8 fF/mm (diffusion)
Estimate dynamic power consumption @ 1 GHz. Neglect wire capacitance and short-circuit current.

## Slide 17: Solution

## Slide 18: Wire RC Delay
Estimate the delay of a 10x inverter driving a 2x inverter at the end of the 1 mm wire. Assume wire capacitance is 0.2 fF/mm and that a unit-sized inverter has R = 10 KW and C = 0.1 fF.
  tpd = (1000 W)(100 fF) + (1000 + 800 W)(100 + 0.6 fF) = 281 ps

## Slide 19: Elmore Delay